Astro
Tutorial (draft)

# Astronomy and computations
## General
Program implements some basic astronomical computations. Given a date and location on the Earth’s surface, it can compute the positions of the fixed body (star). In additions to fixed body position calculations, it computes Julian date, local sidereal time. Also represents raising and setting times, exposition time and coordinates in horizontal system (altitude and azimuth) for selected fixed body object. For all astronomy computations PyEphem library is used. The numerical routines that lie behind PyEphem are those from the wonderful XEphem astronomy application, whose author, Elwood Downey, generously gave permission for us to use them as the basis for PyEphem.
## Configuration
The accurate location of observatory is needed for computation right Apparent Topocentric Position of the fixed body. It can be done through common configuration file “default.conf”, which can be found in programs main folder. Observer configuration located under [observer] section. Latitude and longitude should be presented as float numbers, elevation in meters.

 Default values are:
[observer]
latitude = 58.26574191042049
elevation = 65.42
temperature = 24.0
longitude = 26.4600670337677

## Body position computation
Fixed body position computation take many steps inside PyEphem library, it takes in account observer position. Common calculation flow is follow:

1. Having “star-atas position” of the body PyEphem calculates for choosen epoch Atrometric Geocentic Position
2. Next, PyEphem adjusts the body’s position for relativistic deflection, which is the slight nudge that gravity gives to light that passes very close to the Sun. This only affects objects within about 10° of the Sun and which lie on the far side of it from the Earth.
3. Next, PyEphem adjusts the body’s position for nutation, which is really not an adjustment to the body’s apparent location at all, but a correction for the fact that the platform from which we observe — the Earth — wobbles over the span of months and years. If you want to point a very accurate telescope at an object, then you have to account for this wobble in the Earth’s pole. (Star atlas coordinates always ignore this, and pretend that the Earth’s pole doesn’t have this slight wobble, which is why the “Astrometric” coordinates above don’t have to include this correction.)
4. Next, PyEphem adjusts the body’s position for the aberration of light, the fact that the motion of the Earth through space causes a slight slant to the light reaching us from other objects, in the same way that driving through rain or snow will make the precipitation look like it is coming down diagonally, from in front of you, instead of looking like it is coming straight down from overhead. (PyEphem skips this step for the Moon, since the Moon travels with the Earth through space.)
5. Having made all of these adjustments, PyEphem is now confident that it knows the direction in which the object appears to lie from the Earth, so it stores the computed Apparent Geocentric Position.
6. The first adjustment that PyEphem makes based on the location of the Observer is to correct for parallax. This is needed because all of the previous steps computed where the body lies when viewed from the location of the Earth itself in its orbit — that is, from the Earth’s exact center, which is why the previous coordinate sets were all named “Geocentric” (the Greek prefix geo- means Earth). But someone on the Earth’s surface is more than 6,300 kilometers away from the Earth’s center, which will shift, very slightly, the position of Solar System bodies against the background of stars (and will move nearby bodies like the Moon, or an artificial Earth satellite, even more). The parallax correction adjusts for this.
7. Finally, the very atmosphere through which we view the sky acts as a lens that displaces the positions of bodies when they get close to the horizon. PyEphem has to correct for this refraction both in order to give you a more accurate idea of where to point your telescope, and to be able to make correct predictions of rising and setting times.
8. Based on this all calculations PyEphem computes Apparent Topocentric Position.

# Working with GUI interface
## General
AstroLab program was created to implement automatic position control and monitor telescope status. It allows to store star position coordinates in database and user them to telescope navigation. AstroLab keeps continuous connection with PLC controller, what allows to monitor telescope state in real time, such as connectors statuses, alarms, different service parameters.
## Overview
At very first start main window looks like Fig. 1. Telescope and Status panels fields will be empty, if connection is not established yet some fields will be empty. Setpoint panel can be missed, if remote or object control is taken.

Fig 1: Main window
The main window separate logically into independent blocks – panels. Time&Date panel represents local time for observation position. System calculates local sidereal time depend on observer configuration. Telescope panel shows current telescope state, such as selected control mode, service mode, connection status and temperatures in tube and in dome. Status panel represents common system states, such as switchers, subsystem states. Object, Positioning, Control and Setpoint panels are needed to select or enter observation object coordinates and start telescope moving. Depend on control mode manual positioning panel can be hidden.

Object (star) adding, editing
You can add new object to database through menu Object/Edit Objects or by using shortcut ctrl+e. Dialog window should appear on the main view (fig. 2)

Find field filters search result set by input.
Fig 2: Edit dialog
You can add new object by pressing Add button or edit selected object by double click on star name (fig. 3). For coordinate input formating colon separation is used. For example degrees coordinate 10:10:10 means 10 deg 10 min 10 sec.

Fig 3: Object update

If coordinate input is wrong Update button become inactive. After pressing update changes will be written into database immediately.
Also you can delete object by selecting object and pressing del button on the keyboard.

Object (star) selection
You can select observation object through menu Object/Select Object or by using shortcut ctrl+o. Dialog window should appear on the main view (fig. 4). The result list is filtering dynamically by inputted name.

Fig 4: Object selection

Selection can be done by pressing Select button or by double click on star name. You also can add new object if you will put unique star name and correct coordinates into fields.

Selected object information
After object selection main view will apply selected object coordinates and show detail information about its current position (fig. 5).
The coordinates (ra, dec) for epoch2000 and current epoch will be displayed in Object panel.
Also telescope altitude and hour angle will be shown.
For every object program tries to calculate Rise and Set times, if it not possible the always or never state will be shown (star is always visible or never sets).

Fig 5: Selected object info

Automate telescope moving
After object selected and if object is “visible” for telescope in PC mode you can start to automate moving by pressing Move button. The aim position will be shown in Positioning panel, you can also track telescope current position by using this panel.
1. Manual mode
Astro program supports two main modes: auto and manual.
If manual control is needed, you can catch control by selection Manual mode (Auto/Manual button).
In control panel you can manually move telescope by using keyboard arrows or corresponding buttons.

Time & Date panel
Time and Date panel shows local time, Greenwich time, Julian date and Sidereal time (GST not LST)

Interface is totally translatable in can be translated into any language.