AstroLab
Tutorial (draft)

# Astronomy and computations
## General
Program implements some basic astronomical computations. It computes the positions of the fixed body (star) for a given date and location on the Earth’s surface. In addition to fixed body position calculations, it computes Julian date, Local Sidereal Time. It also represents the raising and setting times, the exposition time with horizon level offset and coordinates in horizontal system (altitude and azimuth) for selected fixed body object. For all astronomy computations PyEphem library is used. The numerical routines that lie behind PyEphem are those from the XEphem astronomy application, whose author, Elwood Downey.
## Body position computation
Fixed body position computations take many steps inside PyEphem library. It takes in account observer position for computations of the current fixed body location in the sky. Common calculation flow is described below:
1. Having “star-atas position” of the body PyEphem calculates for chosen epoch Astrometric Geocentric Position
2. Next, PyEphem adjusts the body’s position for relativistic deflection, which is the slight nudge that gravity gives to light that passes very close to the Sun. This only affects objects within about 10° of the Sun and which lie on the far side of it from the Earth.
3. Next, PyEphem adjusts the body’s position for nutation, which is really not an adjustment to the body’s apparent location at all, but a correction for the fact that the platform from which we observe — the Earth — wobbles over the span of months and years. If you want to point a very accurate telescope at an object, then you have to account for this wobble in the Earth’s pole. (Star atlas coordinates always ignore this, and pretend that the Earth’s pole doesn’t have this slight wobble, which is why the “Astrometric” coordinates above don’t have to include this correction.)
4. Next, PyEphem adjusts the body’s position for the aberration of light, the fact that the motion of the Earth through space causes a slight slant to the light reaching us from other objects, in the same way that driving through rain or snow will make the precipitation look like it is coming down diagonally, from in front of you, instead of looking like it is coming straight down from overhead. (PyEphem skips this step for the Moon, since the Moon travels with the Earth through space.)
5. Having made all of these adjustments, PyEphem is now confident that it knows the direction in which the object appears to lie from the Earth, so it stores the computed Apparent Geocentric Position.
6. The first adjustment that PyEphem makes based on the location of the Observer is to correct for parallax. This is needed because all of the previous steps computed where the body lies when viewed from the location of the Earth itself in its orbit — that is, from the Earth’s exact center, which is why the previous coordinate sets were all named “Geocentric” (the Greek prefix geo- means Earth). But someone on the Earth’s surface is more than 6,300 kilometers away from the Earth’s center, which will shift, very slightly, the position of Solar System bodies against the background of stars (and will move nearby bodies like the Moon, or an artificial Earth satellite, even more). The parallax correction adjusts for this.
7. Finally, the very atmosphere through which we view the sky acts as a lens that displaces the positions of bodies when they get close to the horizon. PyEphem has to correct for this refraction both in order to give you a more accurate idea of where to point your telescope, and to be able to make correct predictions of rising and setting times.
8. Based on these calculations PyEphem computes Apparent Topocentric Position.

# Configuration
## General
AstroLab allows to change and adjust some parameters of work through configuration files and configuration menu. There are two configuration files in root folder: default.conf and plc.conf. By changing default.conf you can adjust database connection parameters, observer position and common program parameters, such as selected language and logging time. The common parameters can also be changed through configuration menu.
## Observer
The accurate location of observatory is needed for correct computation of Apparent Topocentric Position of the fixed body. It can be done through common configuration file “default.conf”, which can be found in the program's main folder. Observer configuration is located under [observer] section. Latitude and longitude should be presented as float numbers, elevation in meters. Horizon can be any degree in the following format - DEG:MIN:SEC
Default values are:
[observer]
latitude = 58.26574191042049
longitude = 26.4600670337677
elevation = 65.42
horizon = 00:04:00

## Database
AstroLab uses MySQL database, which is located on the same host, as the program. This can be easily changed by reconfiguration of database connection. It can be done through common configuration file “default.conf”, which can be found in program's main folder.
Default values are:
[db configuration]
database = astro
host = localhost
user = astro
password = 5gh6w35
port = 3306

PS! In spite of any SQL database support and opportunities for changing connection parameters, correct work of program is not assured.
## PLC configuration
AstroLab holds continuous connection with main PLC block. The connection parameters can be changed in “plc.conf” file.
Default values for PLC block connection are:
[connection]
#tqravere
host = 193.40.1.221
slave id = 1
port = 502

PS! Do not change any values, if you do not know, what you do.

# Working with GUI interface
## General
AstroLab program was created to implement automatic position control and monitor telescope status. It allows to store atlas star position coordinates (in epoch J2000) in database and use their coordinates to navigate a telescope. AstroLab keeps continuous connection with PLC block and database. This allows to monitor telescope state in real time (the maximum delay less than 0.5 sec) . AstroLab monitors connection statuses, alarms, different service parameters and states. The GUI can be switched to any language. However, this particular manual is oriented on the English version.
## Date and angle representation
All calculations with angle are performed in radians. For increasing human readability in configuration files and program's GUI the following format is used:
   HH:MIN:SEC represents hour angles, for example right ascension.
   DEG:MIN:SEC represents degree angle, for example declination or altitude.
## Overview
At the very first start of the program the main window looks like Fig. 1.
The main window is separated logically into the independent parts – panels: Object panel, Positioning, Control panel, Setpoint panel, Time&Date panel, Telescope panel, State panel. Telescope and Status panel's fields will be empty, if connection is not established yet. Setpoint panel can be missed, if remote or object control is taken.

Fig 1: Main window

### Object panel
Object panel is the most important panel in the program. It holds all common information about observation object. Original and current position in equatorial and horizontal coordinate systems (topocentric positioning is used). Program automatically calculates current object position in sky, makes all corrections and puts this new position value into the set-point. By clicking the start button in Control panel user sends this set-point value to PLC and telescope starts moving.
Raising and setting times are represented, if their calculation is possible from observation point. In other case “N/A” message will be displayed. This can occur in two cases, if star is never setting or raising. Exposition time is calculated as the difference between setting and current times. “N/A” will be displayed, if setting time is missed. This time values are corrected on horizon level, which can be set up in configuration file.
Hour angle (HA) is calculated as the difference between Local Sidereal Time (LST) and local right ascension (RA). To determine objects visibility, the program compares current object altitude value with the horizon level.
### Positioning panel
Positioning panel is used to represent the current telescope axes positions in equatorial system. The hour angle value and dome position are also shown in positioning panel, in addition to the right ascension and declination. For representing angles, default format is used: HH:MIN:SEC and DEG:MIN:SEC.
The focus is represented only for current position, because the focus control is done through remote control. Focus value is represented in millimeters.
### Control panel
Control panel gives the basic controls of the telescope. It is possible to take the control by choosing Object's or Manual set-point source. After that “Control mode” value in Telescope panel should change to “PC”. In some special cases “PC control” is not allowed, in that case “Remote control” will be taken back.
By clicking Start and Stop buttons the start and stop command will be sent to PLC controller immediately. If telescope is not movable (see Telescope panel, Movable status) Start button will be disabled. If telescope is moving, the start button will be also disabled.
### Setpoint panel
Setpoint panel adds opportunity to set set-point for telescope manually. Having chosen object from database in “Object's setpoint” mode, the program automatically calculates current object position in sky, makes all corrections and puts this new position value into set-point. By clicking start button in Control panel user sends this set-point value to PLC block and telescope starts moving.
If “Manual setpoint” mode is selected, the program will take the inputted values and send them directly to PLC block without any corrections and compensations.
### Time&Date panel
Time&Date panel represents local and Greenwich times, Julian date and Sidereal time for observation position. System calculates Local Sidereal time (LST) and Julian date (JD) based on observer configuration.
### Telescope panel
Telescope panel shows current telescope status. Two connection statuses check connection with main PLC block and secondary PLC block every 2 sec. The movable status informs about general telescope readiness state. All consistency checks are implemented by first PLC block and telescope moving will be blocked until all requirements are met. Move/Stop status just represent the current telescope moving status.
There are two main modes for telescope: work and service. Working with telescope through PC program is allowed only in the work mode.
The control of telescope can be done in different places, such as: PC room, Observation room, Telescope room or with remove control. The current selected control mode is represented in telescope panel too.
### Status panel
Status panel represents common system states, such as switchers and trailers, subsystem states. Monitoring of this states, can help to find the most common failures and reasons, why they occur.

## Working with objects
AstroLab operates only with equatorial coordinates of stars in epoch J2000 format. Most operations with stars are performed in “Edit Object” dialog, which can be open through menu “Object/Edit Object” or by pressing shortcut “Ctrl+E” (fig. 1). The search result is limited by 1000 objects. You can dynamically filter search result by typing star name in “Find” field. It will help to find the needed objects easier.
Fig 1: Edit object dialog
Coordinates are represented in default standard:
    HH:MIN:SEC for right ascension.
    DEG:MIN:SEC for declination.
For example degrees coordinate 10:10:10 means 10 deg 10 min 10 sec.
### Adding new object
Fig 2: Add star
New object can be easily added through “Editing object” dialog by clicking “Add” button. “Add star” dialog should appear with 3 input fields: star name, star ra and dec position in J2000 format. The “Add” button will be disabled until you enter correct RA and DEC values with the unique object name.

### Changing object
Fig 3: Change object
The coordinates of the object can be changed by double click on object in “Edit Object” dialog. (fig. 1). Only the coordinates can be changed. The “Update” button will be disabled until you enter correct RA and DEC values. After pressing “Update” button the changes will be written into database immediately.

## Object selection

Fig 4: Object selection
Object selection can be performed from “Select Object” dialog, which can be opened from menu bar “Object/Select Object” or by pressing shortcut “Ctrl+O”.
Dialog consists of two parts: the list of stored objects from database on the right and selected object parameters on the left. The list of objects can be dynamically filtered by typing needed object name. The object can be selected by double click on the needed object from the list or by pressing “Select” button. “Select” button will be disabled, if object is not selected from the list.
Important! If object is stored in database, program will load the actual object parameters from database after selection as set-point values. If you select object from list or enter existing object name and change its coordinates, it will no affect the computations.
Important! If you enter new name with right coordinates on selection, you will be asked to if you want or not to store this object. Process will continue only with the stored object! If you need to check some coordinates, please, use “Manual setpoint” mode.
Fig 1: Select object data
After object selection the “Object Panel” will be filled by actual object position data. The atlas and current equatorial position will be shown. In addition to equatorial coordinates, horizontal coordinates will be calculated too. The next rising and setting times with exposition time will be calculated and corrected to horizon level. Hour angle will be calculated for the current moment of time for actual Sidereal time.